## Slide 1: Percs vs. Paddles: Pearls and Pitfalls
Alon Y. Mogilner, MD, PhD
Director, Center for Neuromodulation
Associate professor of Neurosurgery and Anesthesiology
NYU Langone Medical Center
New York, NY

## Slide 2: Disclosures
Consultant, Honorarium:
  Medtronic
  Abbott/St. Jude
  Alpha-Omega Engineering
Gammacore - Equity Share

## Slide 3: Overview
Both percutaneous and paddle leads can be appropriate and viable options for spinal cord stimulator implantation
We will review:
  Hardware fundamentals
  Basic surgical technique
  Literature
  Complications and outcomes via representative cases

## Slide 4: SCS leads
Percutaneous:
  Thin, cylindrical leads placed via a needle
  Can be placed by non-surgeons
  Non-insulated (stimulation spreads 360º)
Paddle:
  Wider, rectangular leads
  Must be placed surgically via laminotomy
  Insulated
NOTE: DRG leads are only percutaneous at this time

## Slide 5: SCS Trials
Percutaneous, unless the epidural space cannot be accessed via a needle (i.e. prior decompression, fusion, etc.)
Epidural space accessed below levels of final contact locations (i.e. L2-3 access for T8-9 lead placement)

## Slide 8: Trust, but verify…
Review all preoperative imaging carefully and correlate with operative notes
If you cannot see the T12-L1 junction clearly, make the referring physician and patient aware…

## Slide 9: Permanent Implant: Percutaneous vs. Paddle
Determined on a patient-by-patient basis
  Percutaneous:
    Advantages:
      Less incisional pain
      Same day discharge in all cases (barring complications)
    Disadvantages:
      Lead migration
      Less efficient energy use
  Paddle:
    Advantages:
      Minimal risk of migration
      More efficient energy delivery
    Disadvantages:
      More painful
      May not be safe in cases of canal stenosis

## Slide 10: SCS Paddle Electrodes

## Slide 12: SCS Paddle Electrode Placement with Monitoring
Allows for physiologic assessment of lead location
Presumably provides a measure of safety to minimize neurologic deficit secondary to spinal cord injury
No evidence that awake with feedback is any safer than asleep placement, with or without monitoring

## Slide 13: Paddle leads: Pitfalls
60 YO male referred to me 4 months after paddle lead placement for FBSS by another surgeon
Soon after lead placement, developed severe left-sided chest wall pain
In and out of ER, ruled out for PE and MI
Pain was noted to be positional, worsening with extension
Presents to me three months postop

## Slide 14: Case 3

## Slide 15: Neural Compression

## Slide 16: Paddle leads and compression
Paddle leads placed eccentrically, or even placed in the midline in patients with stenosis, can cause severe radicular pain.
If the pain does not resolve, either removal of the lead or a further decompression is the only way to treat these symptoms •Spinal MRI recommended prior to all paddle placements (CT myelo if MRI not possible)

## Slide 17
Lead Placement: Not always straightforward

## Slide 18: Paddle Placement
Epidural scar tissue, scoliosis, or other factors can prevent appropriate midline electrode placement…
This can be a particular problem with revisions from percutaneous to paddle, and with longer paddles
Surgical strategies…
  First do no harm…

## Slide 19
Complete Decompression…

## Slide 20
A full laminectomy over the paddle may be necessary at times
Anchoring technique:
  lead edges tucked under bone
  Tisseel fibrin glue placed over lead
Complete Decompression…

## Slide 21: Partial Decompressions
Based on the anatomy and the location of the obstructions, partial decompressions can facilitate appropriate lead placement…
Why is the lead not passing?
  Where is/are the obstructions?

## Slide 23: What not to do
50 YO male referred to a neurosurgeon for a permanent implant s/p successful percutaneous trial
Trial lead spanned T8-T10
T8
T9

## Slide 24
T8-9 Disc space

## Slide 28: Cervical SCS placement
I have moved away from cervical paddle placement
Exceptions:
  Inability to access the cervical epidural space percutaneously
  Multiple (>2) lead migrations

## Slide 30: Cervical SCS
47 YO female with unilateral UE CRPS
Had successful percutaneous SCS trial
Referred for permanent implant
How would you implant?
•Non-myelopathic

## Slide 32: Implant
Patient undergoes cervical laminectomy and anterograde lead placement
Wakes up with severe pain and weakness in the arm
Told it is an exacerbation of her CRPS and sent home
Eventually, strength recovers but remains with new neuropathic pain qualitatively different than her preop pain

## Slide 34: Options for cervical paddle placement
Retrograde C1-C2 placement

## Slide 35: Cervical SCS
51 Y/O male with brachial plexus injury
Unilateral RUE pain
•Percutaneous trial attempted but aborted due to severe radiculopathy and pain while passing lead
Referred to me

## Slide 37: Cervical SCS case 2
36 YO female with bilateral UE neuropathic pain
Had successful percutaneous SCS trial
•Had a percutaneous system placed by another physician (anesthesia pain assisted by spinal neurosurgeon)
•Lead migration 6 months later
Referred for revision implant
How would you implant?

## Slide 38: Cervical SCS Case 2
Underwent retrograde C1-2 lead placement by another physician

## Slide 39: Implant
Patient undergoes retrograde C1-2 lead placement
Wakes up with severe pain, spasms and weakness in the right arm
Told it is an exacerbation of her condition and sent home

## Slide 40: Case 2, continued
Case “run by me” by the pain physician
System not MRI compatible
Myelo CT…

## Slide 41
Underwent device removal, followed by C-Spine MRI
Referred to me…
Original preoperative pain has returned (bilateral)
Superimposed on this is new right arm “spasms”

## Slide 42
• No area is truly safe in the cervical spine, although it seems some are safer than others

## Slide 43: Summary
Trials: percutaneous unless epidural space cannot be accessed
Permanent:
  Cervical: percutaneous unless not possible
  Thoracic:
    Canal diameter
    Age
    Body Habitus
    Activity level
    Comorbidities

## Slide 44
Thank you